## Slide 1: Water pollution and air pollution

## Slide 2: WATER QUALITY - CRITERIA AND STANDARDS
The WHO has published in 1993 vol.l and in 1996 vol. 2 of second edition, and more recently vol. I and II in 2011 of guidelines for drinking water quality intended for use by countries as a basis for the development of standards, which, if properly implemented, will ensure the safety of drinking water supplies. In order to define standards, it is necessary to consider these recommendations in the context of prevailing environmental, social, economic and cultural conditions.
These guidelines are intended to supersede the guidelines for drinking water published in 1984.
The guidelines for drinking water quality recommended by WHO (2011) relate to following variables :
I Acceptability aspects.
II Microbiological aspects.
III Chemical aspects.
IV Radiological aspects.

## Slide 3: I. ACCEPTABILITY ASPECTS
A. Physical parameters :
Turbidity
Colour
Taste and odour
Temperature

## Slide 4
B. Inorganic constituents :
Chlorides
Hardness
Ammonia
pH
Hydrogen sulphide
Iron
Sodium sulphate
Total dissolved solids
Zinc
Manganese
Dissolved oxygen
Copper
Aluminium

## Slide 5: II. MICROBIOLOGICAL ASPECTS
Bacteriological indicators :
Coliform organisms.
Faecal streptococci
Cl. Perfringens
Virological aspects
Biological aspects

## Slide 6: III. CHEMICAL ASPECTS
Inorganic chemicals of health significance in drinking water
Constituents Recommended maximum limit of concentration
(mg/litre) (Mg/litre)
Antimony 0.02 (P) 20
Arsenic 0.01 (P) 10
Barium 0.7 700
Boron 2.4 2,400
Cadmium 0.003 0.3
Chromium 0.05 (P) 50
Copper 2 2,000
Fluoride 1.5 1,500
Lead 0.01 10
Manganese 0.4 (P) 400
Mercury (total) 0.006 6
Molybdenum 0.07 70
Nickel 0.07 70
Nitrate (as NO3) 50 50,000
Nitrite (as NO2) 3(P) 3,000
Selenium 0.04 40

## Slide 7: Organic constituents
Organic constituents Upper limit of concentration
(pg/litre)
Chlorinated alkanes
Carbon tetrachloride 2
Dichloromethane 20
Chlorinated ethenes
Vinyl chloride 55
1.1 – dichloroethane 30
1.2 - dichloroethene 50
Aromatic hydrocarbons
Benzene 10
Toluene 700
Xylenes 500
Ethylbenzene 300
Styrene 20
Benzolalpyrene 0.7

## Slide 8: Pesticides :
Guideline values of certain pesticides
Pesticides Upper limit of concentration (pg/litre)
Aldrin/dieldrin 0.03
Chlordane 0.2
DDT 2 2,4-D 30
Heptachlor and heptachlor epoxide 0.03
Hexachlorobenzene 1
Lindane 2
Methoxychlor 20
Pentachlorophenol 9

## Slide 9: Polynuclear aromatic hydrocarbons :
The following recommendations are made for the PAH group :
Because of the close association of PAH with suspended solids, the application of treatment, when necessary to achieve the recommended level of turbidity will ensure that PAH levels are reduced to a minimum.
Contamination of water with PAH should not occur during water treatment or distribution. Therefore, the use of coal-tar-based and similar materials for pipe lining and coatings on storage tanks should be discontinued.
In situation where contamination of drinking water by PAH has occurred, the specific compounds present and the source of the contamination should be identified, as the carcinogenic potential of PAH compounds varies.

## Slide 10: Drinking water consumption and body weight
Health-risk assessment
Tolerable daily intake (TD1)
Acceptable daily intake (ADI)
No-observed-adverse-effect level (NOAEL)
Lowest-observed-adverse-effect level (LOAEL)
Uncertainty factors (UF)

## Slide 11: RADIOLOGICAL ASPECTS
The activity of a radio-active material is the number of nuclear disintegration per unit of time. The unit of activity is a becquerel (Bq); 1 Bq = 1 disintegration per second. Formerly, the unit of activity was curie (Ci).
The proposed guideline values are :
gross alpha activity 0.5 Bq / L
gross beta activity 1.0 Bq / L

## Slide 12: SURVEILLANCE OF DRINKING WATER QUALITY
The activities that ideally should be included in the surveillance function are :
a. approval of new sources (including private-owned supplies).
b. watershed protection.
c. approval of the construction and operating procedures of waterworks, including :
(i) disinfection of the plant and of the distribution system after repair or interruption of supply,
(ii) periodic flushing programmes and cleaning of water storage facilities,
(iii) certification of operators,
(iv) regulation of chemical substances used in water treatment,
(v) cross-connection control, back-flow prevention and leak detection control;

## Slide 13
d. sanitary surveys; e. monitoring programmes, including provision for central and regional analytical laboratory services;
f. development of codes of practice for well construction, pump installation and plumbing; g. inspection quality control in bottled-water and ice manufacturing operations.

## Slide 14
Surveillance of drinking water is essentially a health measure. It is intended to protect the public from waterborne diseases.
The elements of a surveillance programme are :
Sanitary survey
Sampling
Bacteriological surueillance
PRESUMPTIVE COLIFORM TEST
Multiple tube method
Confirmatory tests
Membrane filtration technique
THE DETECTION OF FAECAL STREPTOCOCCI AND Cl. PERFRINGENS
COLONY COUNT
Biological examination
Chemical surveillance

## Slide 15: HARDNESS OF WATER
Hardness may be defined as the soap destroying power of water. The consumer considers water hard if large amounts of soap are required to produce lather. The hardness in water is caused mainly by four dissolved compounds.
These are
(1) Calcium bicarbonate
(2) Magnesium bicarbonate
(3) Calcium sulphate, and
(4) Magnesium sulphate.
Hardness is classified as carbonate and non-carbonate. The carbonate hardness which was formerly designated as “temporary” hardness is due to the presence of calcium and magnesium bicarbonates. The non-carbonate hardness, formerly designated as “permanent” hardness, is due to calcium and magnesium sulphates, chlorides and nitrates.

## Slide 16
Hardness in water is expressed in terms of “milllequivalents per litre (mEq/L)”. One mEq/L of hardnessproducing ion is equal to 50 mg CaCO3 (50ppm) in one litre of water.
Classification of hardness in water:
Soft water less than 1(<50 mg/L)
Moderately hard water 1-3 (50-150 mg/L)
Hard water 3-6 (150-300 mg/L)
Very hard water above 6 (>300 mg/L)

## Slide 17: Disadvantages of hardness
Hardness in water presents several disadvantages both to the domestic and industrial consumer. These may be stated as follows:
(1) hardness in water consumes more soap and detergents
(2) when hard water is heated, the carbonates are precipitated and bring about furring or scaling of boilers. This leads to great fuel consumption, loss of efficiency and may sometimes cause boiler explosions
(3) hard water adversely affects cooking; food cooked in soft water retains its natural colour and appearance
(4) fabrics washed with soap in hard water do not have a long life
(5) there are many industrial processes in which hard water is unsuited and gives rise to economic losses
(6) hardness shortens the life of pipes and fixtures.

## Slide 18: Removal of hardness
The methods of removal of hardness are briefly stated as below:
Temporary hardness
(a) Boiling
(b) Addition of lime
(c) Addition of sodium carbonate
(d) Permutit process.
Permanent hardness
(a) Addition of sodium carbonate
(b) Base exchange process.

## Slide 19: Fluoridation of water
Fluorine is one of the constituents naturally present in water supplies. The main source of fluorine is drinking water.
Deficiency of fluorine in drinking water is associated with dental caries, and excess with dental and skeletal fluorosis.
Leading workers in India regard fluorine in concentration of 0.5 to 0.8 ppm in drinking water as optimum (a concentration of 1 ppm is regarded as optimum in temperate climates because the consumption of water is low).
The term “fluoridation” has been given to the process of supplementing the natural fluoride content of potable waters to the point of optimum concentration.
The WHO in 1969 recommended fluoridation of community water supplies in areas where the total intake of fluorides by the population is below the optimal levels for protection against dental caries.
Fluoridation is now an accepted public health procedure in many developed countries

## Slide 20: SELECTION OF SOURCE OF WATER
In selecting a source, attention must be given to possible future developments that may influence the continued suitability of the source. Other considerations include :
(a) Quantity (source capacity): The quantity of water should be sufficient to meet continuing water demands, taking into account daily and seasonal variations and projected growth in the size of the community being served,
(b) Quality : The quality of raw water should be such that, with appropriate treatment it meets the drinking water standards,
(c) Protection : The watershed must be protected from pollution with human excreta, industrial discharge and agricultural run-off.
(d) Feasibility : The source should be available at reasonable cost,
(e) Treatability : The raw water should be treated adequately under locally prevailing conditions.

## Slide 21: DISTRIBUTION OF WATER
There are two main systems of water distribution, the intermittent supply and the continuous supply.
In the intermittent system, water is delivered only during fixed hours. The disadvantages of the intermittent system are :
(1) the pipes may be empty during times of emergency
(2) people need to store water in containers which may not be clean always. The safe water is likely to be rendered unsafe through improper storage
(3) when the pipes are empty, there is negative pressure and by what is known as back-siphoning, bacteria and foul gases may be sucked in through leaky joints.
A number of recorded outbreaks of typhoid and of relapsing fever, among other diseases, have been traced back to the contamination of water in the intermittent piped water supplies. Flowing water available 24 hours is therefore desirable, although it may entail some wastage of water through misuse. The supply of water in most cities in India is intermittent. A WHO Expert Committee (1965) strongly recommended that intermittent and low pressure service should be avoided.

## Slide 22
DUAL WATER SUPPLY:
In Kolkata, there was a dual water supply system, i.e., one set of pipes supplying filtered water for personal use and the other set supplying unfiltered water for flushing toilets, washing roads and other civic purposes.
The greatest drawback of the dual system is that people may mistake one for the other through ignorance. The WHO Expert Committee (1965) strongly disapproved of the practice of supplying two kinds of water. The possibility of cross-connection constitutes a serious health hazard.

## Slide 23: SWIMMING POOL SANITATION
Swimming pool water is exposed to :
(1) faecal contamination and
(2) organisms from skin and nasopharynx.
The health hazards associated with swimming pools are:
fungal and viral infections of the skin. This includes Epidermophyton and Trichophyton species which produce “athlete’s foot.” The papilloma virus is the inciting agent of “plantar warts”
infections of the eye, ear, nose and throat
(3) infections of the upper respiratory tract,
(4) intestinal infections, and
(5) accidents

## Slide 24: National Water Supply and Sanitation Programme
The National Water Supply and Sanitation Programme was launched in 1954 by the Govt, of India as part of the Health Plan to assist the States to provide adequate water supply and sanitation facilities in the entire country.
Provision has been made in the successive 5-year Plans to improve the water supply.

## Slide 26: Air pollution

## Slide 27: Composition
Air is a mechanical mixture of gases. The normal composition of external air by volume is approximately as follows:
Nitrogen - 78.1 per cent
Oxygen - 20.93 per cent
Carbon dioxide - 0.03 per cent.
The balance is made up of other gases which occur in traces, e.g., argon, neon, krypton, xenon and helium. In addition to these gases, air also contains water vapour, traces of ammonia and suspended matter such as dust, bacteria, spores and vegetable debris.

## Slide 28
Air is rendered impure by :
(1) Respiration of men and animals
(2) Combustion of coal, gas, oil, etc.
(3) Decomposition of organic matter and
(4) Trade, traffic and manufacturing processes which give off dust, fumes, vapours and gases.
Under ordinary conditions, the composition of outdoor air is remarkably constant. This is brought about by certain self-cleansing mechanisms which operate in nature
(1) Wind : Wind dilutes and sweeps away the impurities by its movement. Because of wind movement, impurities do not accumulate in any one place;
(2) Sunlight: The atmospheric temperature and sunlight play their own part by oxidizing impurities, and killing bacteria;
(3) Rain : It cleanses the atmosphere by removing the suspended and gaseous impurities;
(4) Plant life : The green plants utilize fhe carbon dioxide and generate oxygen; this process is reversed during the night time. When the rate of pollution becomes too high or when the cleansing process becomes Ineffective, it constitutes a health hazard.

## Slide 29: The air of occupied room
Human occupancy and activity vitiate air in occupied rooms and give a sense of discomfort to the occupants. The changes in air that take place in confined places are both chemical and physical,
(a) CHEMICAL CHANGES The air becomes progressively contaminated by carbon dioxide and the oxygen content decreases due to metabolic processes.
An average person at rest gives off 0.7 c.ft of carbon dioxide per hour; this may increase up to 2 c.ft. during physical activity.
In a mixed gathering comprising all age groups, the per capita output of carbon dioxide is taken as 0.6 c.ft. per hour.

## Slide 30
(b) PHYSICAL CHANCES : The most important changes that occur due to human occupancy are the physical changes. These are
(i) Rise in temperature
(ii) Increase of humidity
(iii) Decrease in air movement
(iv) Body odor
(v) Bacterial pollution : The exhaled air contains microorganisms in suspension. These are principally saprophytic bacteria and may include pathogenic bacteria. These organisms are discharged into the air during conversation, coughing, sneezing and loud talking.