## Slide 1: Safe Water Provision in India

## Slide 2: As usual…
Which of the following is a water-washed disease?
  Trachoma
  Leptospirosis
  Acute Hepatitis A
  Legionnaire’s Disease

## Slide 3: As usual…
Which of the following is a water-washed disease?
  Trachoma
  Leptospirosis
  Acute Hepatitis A
  Legionnaire’s Disease

## Slide 4: Sources of Water
Surface water
Rain
Rivers & streams
Impound-ing reservoirs
Tanks & ponds
Ground water
Shallow wells
Deep wells
Springs
None in India, Used in Gibralter
Mumbai, Chennai, Nagpur
Delhi, Kolkata, Allahabad, Bhopal
Some villages
Lakes
Bhopal
Sea water
Costly to desalinate
Chandi-garh
In most villages
Hilly areas

## Slide 5: Quiz
Purest water in nature is from
  Rains
  Lakes
  Ponds
  Springs

## Slide 6: Quiz
Purest water in nature is from
  Rains
  Lakes
  Ponds
  Springs

## Slide 7: Quiz 2
While collecting water for biological testing, which of the following should NOT be done?
  Using sterile container
  Sealing the top with paper
  Discarding the initial water from source
  Cleaning the container before sample collection

## Slide 8: Quiz 2
While collecting water for biological testing, which of the following should NOT be done?
  Using sterile container
  Sealing the top with paper
  Discarding the initial water from source
  Cleaning the container before sample collection

## Slide 9: Concept of Safe Water
Free from pathogens
Free from harmful chemical substances
Pleasant to taste (free from bad odour or taste)
Usable for domestic purposes

## Slide 10: Safe Drinking Water can have..
Improved Sources
Piped household
Public standpipe
Borehole
Protected dugwell
Protected spring
Rainwater collection
Unimproved Sources
Unprotected dug-well
Unprotected spring
Surface water (river, dam, lake, pond, stream, canal, irrigation channel)
Vendor-provided water (carts, tanker truck etc)
Bottled water*
Bottled water is not considered improved due to limitations in the potential quantity, not quality, of the water

## Slide 11: Legal Commitment!
The provision of clean drinking water has been given priority in the Constitution
Article 47 conferring the duty of providing clean drinking water and improving public health standards to the State (i.e. Indian Union)

## Slide 12: Indian Government norms for Water
Availability of 40 litres of safe drinking water per capita per day for rural areas, AND
At least one hand-pump / spot-source for every 250 persons

## Slide 13: Quiz
Vital layer is present in
  Slow sand filter
  Rapid sand filter
  Reverse osmosis filter
  Solar distillation apparatus

## Slide 14: Quiz
Vital layer is present in
  Slow sand filter
  Rapid sand filter
  Reverse osmosis filter
  Solar distillation apparatus

## Slide 15: Availability of Drinking Water Resources (Census 2011)..
S No | Availability | India | Madhya Pradesh
1 | Within the Premises | 46.6% | 23.9%
2 | Near the Premises | 35.8% | 45.6%
3 | Away from the Premises | 17.6% | 30.5%
More information available at http://indiawater.gov.in/IMISReports/
94 % of the rural population and 91 % of the people living in urban areas have access to safe drinking water

## Slide 17: Miles to go before we sleep..
Fine, should we focus on problems rather than “achievements”?
Problems
  Unsafe water
  Unimproved water
  Unpalatable water

## Slide 18: Burden of Unsafe water
1.5 million children die of diarrhoea per year
37.7 million cases of waterborne diseases annually
73 million working days are lost annually
$600 million a year is economic loss annually

## Slide 19: Vulnerable Populations..
The rural population
  >700 million people
  residing in about 1.42 million habitations
  spread over 15 diverse ecological regions
Urban slums
Nomadic populations groups

## Slide 20: “Problem Village”
No source of safe water available within a distance of 1.6 kilometers, OR
Water available at depth of more than 15 metres, OR
Water source has excess salinity, iron, fluorides, and other toxic elements, OR
Water exposed to risks of cholera

## Slide 21: Challenges..
The major chemical parameters of concern are fluoride and arsenic
  66 million Indians at risk due to excess fluoride
  10 million due to excess arsenic
Iron and Nitrates are also emerging as major problems

## Slide 22: Quiz
Chlorination does not affect in normal doses
  HIV
  Polio
  Shigella
  Salmonella

## Slide 23: Quiz
Chlorination does not affect in normal doses
  HIV
  Polio
  Shigella
  Salmonella

## Slide 24: Recall what is Safe Water?
Free from pathogens
Free from harmful chemical substances
Pleasant to taste (free from bad odour or taste)
Usable for domestic purposes

## Slide 25: Safe water provision also means that….
Supply
Water is treated to make it safe
Storage
Water is stored to prevent contamination
Retrieval
Water is retrieved to keep it safe
Treatment
Availability
Accessibility
Affordability
Adequate
Improved
Community-level or at level of house
Household level
Covered/ uncovered

## Slide 26: Water Treatment (Purification)
One or more of following measures
  Storage leading to sedimentation
  Filtration
  Disinfection

## Slide 27: Community-level Water Treatment

## Slide 28: Storage & Sedimentation
Impounding in natural/ artificial reservoirs
To prevent further pollution
Removes larger particles
  ~90% of suspended impurities settle in 24 hours
Clear water allows penetration of light
  UV disinfection

## Slide 29: Storage & Sedimentation
Organic matter is oxidized
  Free ammonia to nitrates
Reduction of pathogens
  ~90% of total bacterial count reduces by 5-7 days
Longer period of storage increases growth of algae
  Bad odour & colour
Optimal period for river water is 10-14 days

## Slide 30: Filtration
Sand-filters
  Rapid (Mechanical)
  Slow (Biological)

## Slide 31: Rapid Sand Filter

## Slide 32: Rapid Sand Filter

## Slide 33: Slow Sand Filtration of Tank Water

## Slide 34: Slow Sand Filter Schematics

## Slide 35: Now try to answer..
In a city grappling with reconstruction phase after torrential rain, which method would be better to provide water to its people?
  Slow sand-filter
  Rapid sand-filter

## Slide 36: Disinfection
Doesn’t remove turbidity
Various methods
  Chlorination
  Solar disinfection
  Ozonation
  Reverse osmosis

## Slide 37: Disinfection Methods

## Slide 38: Household level water treatment

## Slide 39: Household level water storage
Rooftop/Ground-level Tanks
Household Containers/ Pots
No storage
  Handpumps
Covered or uncovered

## Slide 40: Storage & Sedimentation
Rural
Wells (open/ covered)
Household containers
Overhead / grounded tanks
  Bricked
  Plastic
None
Urban
Overhead / grounded tanks
  Bricked
  plastic
Household containers
None

## Slide 42: Storage & Sedimentation
Settling
  24-72 hours (eg. Three Pot Method for 2 days)
  Cheap, easy
Coagulation
  2+ hours
  Cheap, difficult to use
  Poor awareness & acceptability
  Natural (eg. Moringa seeds, Strychnos or nirmali etc)
  Chemical (eg. Alum, alum potash)

## Slide 43: Now debate
Which method of sedimentation have you come across in day-to-day life?
The drinking water available in usual restaurants / households in Kerala coloured.

## Slide 44: Filtration
Straining through Clothes
Biosand filters
Ceramic Filters
  Pot
  Candle
Membrane filters

## Slide 45: Membrane Filter
Filtration Type | Pore Size (µm / nm)
Microfiltration (MF) | 0.1-10 µm (1‑1000 nm)
Ultrafiltration (UF) | 0.01-0.1 µm (1‑100 nm)
Nanofiltration (NF) | <0.001 µm (<1 nm)
Reverse osmosis (RO) | <0.001 µm (<1 nm)
(Contaminant Removal Capabilities)

## Slide 46: Disinfection
Boiling
Chlorination
Solar disinfection (SODIS)
Solar distillation
UV disinfection
RO disinfection

## Slide 47: Household level disinfection

## Slide 48: Boiling
Rolling boil for 10-20 minutes
All pathogens are killed at 1000 C*
  Except sporulating organisms (eg Clostridium)
No residual protection
Bland in taste, Smell or colour not changed
Easy, medium cost

## Slide 49: Chlorination*
Most widely used
Contact of 30 minutes
Residual effect
Not effective on some protozoa & helminths
  Cryptosporidium parvum, Ascaris, Schistosoma
Bleaching Powder, Chlorine Tablets, Chlorine Solution, High Test Hypochlorite
*Iodine & PPM are less commonly used methods of chemical disinfection

## Slide 50: Solar Disinfection
Use transparent PET bottle
More effective on bacteria, less on virus & protozoa
Easy & low cost

## Slide 51: Retrieving safe water
Taps and glass
Taps and bottles
Glass dipped
Ladle
????

## Slide 52: Water Retrieval Methods

## Slide 53: Water conservation!!!
Activity | Frequency | Circumstances | Water Used
Toilet | Four flushes per day | Conventional toilet | 3.5–7 gallons per flush
 |  | Ultra-low flush toilet | 1.6 gallons per flush
Shower | Once a day for 5 minutes | Conventional showerhead | 3–8 gallons per minute
 |  | Low-flow showerhead | 2.5 gallons per minute
Bath | Once a day | Full bathtub | 36 gallons
 |  | Tub 1/4 to 1/3 full | 9–12 gallons
Shaving | Once a day | Open tap | 5–10 gallons
 |  | 1 full basin | 1 gallon
Brushing teeth | Twice a day | Open watertap | 2–5 gallons
 |  | Brush and rinse | 1/4–1/2 gallon
1 gallon of water is equal to 3.8 liters

## Slide 54: Water conservation!!!
Activity | Frequency | Circumstances | Water Used
Washing hands | Twice a day | Open watertap | 2 gallons
 |  | 1 full basin | 1 gallon
Cooking‡ | Washing produce | Open watertap | 5–10 gallons
 |  | 1 full kitchen basin | 1–2 gallons
Automatic dishwasher | Once per day-full load | Standard cycle | 10–15 gallons
 |  | Short cycle | 8–13 gallons
Manual dishwashing | Once a day | Open watertap | 30 gallons
 |  | Full basin/wash and rinse | 5 gallons
Laundry§ | 1/3 load a day | Portion of full load | 35–50 gallons per full load
 |  | Full load | 10–15 gallons for a full load
Car washing | Twice a month | Hose with shut-off nozzle | 100 gallons per month
 |  | 5 full, 2-gallon buckets | 20 gallons per month
1 gallon of water is equal to 3.8 liters

## Slide 55: Parting quiz..
Which of the following is NOT a criteria for a PROBLEM VILLAGE?
  Water source has excess iron
  Water exposed to risks of cholera
  Water available at depth of >15 metres
  No source of safe water available within a distance of 5 km

## Slide 56: Parting quiz..
Which of the following is NOT a criteria for a PROBLEM VILLAGE?
  Water source has excess iron
  Water exposed to risks of cholera
  Water available at depth of >15 metres
  No source of safe water available within a distance of 5 km

## Slide 57: any Queries?